## Slide 1
CloudMatrix UB topology: 128 NPUs / 16 Nodes
Sub-plane 0
Sub-plane 1
Sub-plane 2
Sub-plane 3
Sub-plane 4
Sub-plane 5
Sub-plane 6
UB
L2-P0-S0
UB
L2-P0-S1
UB
L2-P0-S15
S2-S14 omitted; same wiring
UB
L2-P1-S0
UB
L2-P1-S1
UB
L2-P1-S15
S2-S14 omitted; same wiring
UB
L2-P2-S0
UB
L2-P2-S1
UB
L2-P2-S15
S2-S14 omitted; same wiring
UB
L2-P3-S0
UB
L2-P3-S1
UB
L2-P3-S15
S2-S14 omitted; same wiring
UB
L2-P4-S0
UB
L2-P4-S1
UB
L2-P4-S15
S2-S14 omitted; same wiring
UB
L2-P5-S0
UB
L2-P5-S1
UB
L2-P5-S15
S2-S14 omitted; same wiring
UB
L2-P6-S0
UB
L2-P6-S1
UB
L2-P6-S15
S2-S14 omitted; same wiring
UB Switch
L1-N0-S0
UB Switch
L1-N0-S1
UB Switch
L1-N0-S2
UB Switch
L1-N0-S3
UB Switch
L1-N0-S4
UB Switch
L1-N0-S5
UB Switch
L1-N0-S6
NPU 0
R0
NPU 1
R1
NPU 2
R2
NPU 3
R3
NPU 4
R4
NPU 5
R5
NPU 6
R6
NPU 7
R7
Node 0: 8 NPUs, 7 L1 switches, 56 NPU-L1 links
UB Switch
L1-N1-S0
UB Switch
L1-N1-S1
UB Switch
L1-N1-S2
UB Switch
L1-N1-S3
UB Switch
L1-N1-S4
UB Switch
L1-N1-S5
UB Switch
L1-N1-S6
NPU 0
R8
NPU 1
R9
NPU 2
R10
NPU 3
R11
NPU 4
R12
NPU 5
R13
NPU 6
R14
NPU 7
R15
Node 1: 8 NPUs, 7 L1 switches, 56 NPU-L1 links
UB Switch
L1-N15-S0
UB Switch
L1-N15-S1
UB Switch
L1-N15-S2
UB Switch
L1-N15-S3
UB Switch
L1-N15-S4
UB Switch
L1-N15-S5
UB Switch
L1-N15-S6
NPU 0
R120
NPU 1
R121
NPU 2
R122
NPU 3
R123
NPU 4
R124
NPU 5
R125
NPU 6
R126
NPU 7
R127
Node 15: 8 NPUs, 7 L1 switches, 56 NPU-L1 links
...
Nodes
2-14
omitted
L1-Nn-Sp connects to L2-Pp-S0 through L2-Pp-S15. Each plane is independent.
Each NPU in Node n connects to L1-Nn-S0 through L1-Nn-S6. Crossings are not junctions.
Per-direction capacity: NPU-L1 = 56 GB/s (2 x 28 aggregated); L1-L2 = 28 GB/s.
128-NPU contest adaptation: retain 16 L2 switches per plane; populate 16 Node-facing ports per L2.

## Slide 2
Node 0: every NPU connects to every local L1 switch
Switch IDs: L1-N0-S0 through L1-N0-S6. All 56 NPU-L1 connections are drawn.
UB Switch
L1-N0-S0
To ALL 16 L2
in Sub-plane 0
UB Switch
L1-N0-S1
To ALL 16 L2
in Sub-plane 1
UB Switch
L1-N0-S2
To ALL 16 L2
in Sub-plane 2
UB Switch
L1-N0-S3
To ALL 16 L2
in Sub-plane 3
UB Switch
L1-N0-S4
To ALL 16 L2
in Sub-plane 4
UB Switch
L1-N0-S5
To ALL 16 L2
in Sub-plane 5
UB Switch
L1-N0-S6
To ALL 16 L2
in Sub-plane 6
NPU 0
Rank 0
NPU 1
Rank 1
NPU 2
Rank 2
NPU 3
Rank 3
NPU 4
Rank 4
NPU 5
Rank 5
NPU 6
Rank 6
NPU 7
Rank 7
Each colored line: one logical bidirectional edge, 56 GB/s in EACH direction.
56 GB/s aggregates the two 910C dies: 28 + 28 GB/s to each local L1 switch.
Per NPU: 7 x 56 = 392 GB/s per direction. No direct NPU-NPU edges are implied.

## Slide 3
One Sub-plane: all 16 L2 switches and all uplinks are expanded
Shown: Node 0, Node 1 and Node 47. Nodes 2-46 repeat the same connections.
L2-P0-S0
28 GB/s
L2-P0-S1
28 GB/s
L2-P0-S2
28 GB/s
L2-P0-S3
28 GB/s
L2-P0-S4
28 GB/s
L2-P0-S5
28 GB/s
L2-P0-S6
28 GB/s
L2-P0-S7
28 GB/s
L2-P0-S8
28 GB/s
L2-P0-S9
28 GB/s
L2-P0-S10
28 GB/s
L2-P0-S11
28 GB/s
L2-P0-S12
28 GB/s
L2-P0-S13
28 GB/s
L2-P0-S14
28 GB/s
L2-P0-S15
28 GB/s
UB Switch
L1-N0-S0
NPU
0
NPU
1
NPU
2
NPU
3
NPU
4
NPU
5
NPU
6
NPU
7
UB Switch
L1-N1-S0
NPU
0
NPU
1
NPU
2
NPU
3
NPU
4
NPU
5
NPU
6
NPU
7
UB Switch
L1-N47-S0
NPU
0
NPU
1
NPU
2
NPU
3
NPU
4
NPU
5
NPU
6
NPU
7
Each L1: 16 independent uplinks x 28 GB/s = 448 GB/s per direction.
Plane 0: L2-P0-S0 through L2-P0-S15 connect to L1-N0-S0 through L1-N47-S0.
For the 128-NPU contest: use Nodes 0-15 with the same plane wiring; remaining L2 ports are unused.