## Slide 1
A5 1D-FullMesh + Clos: 128 NPUs / 2 cabinets
Each cabinet: 8 Nodes x 8 NPUs, 8 L1 switches. Both cabinets share 4 L2 switches.
Each NPU connects to all 8 local L1 switches. Each L1 connects to all 4 L2 switches.
UB Switch
L2-P0-S0
UB Switch
L2-P0-S1
UB Switch
L2-P0-S2
UB Switch
L2-P0-S3
Cabinet 0: 64 NPUs
UB Switch
L1-C0-S0
UB Switch
L1-C0-S1
UB Switch
L1-C0-S2
UB Switch
L1-C0-S3
UB Switch
L1-C0-S4
UB Switch
L1-C0-S5
UB Switch
L1-C0-S6
UB Switch
L1-C0-S7
...
Nodes
1-6
omitted
Cabinet 1: 64 NPUs
UB Switch
L1-C1-S0
UB Switch
L1-C1-S1
UB Switch
L1-C1-S2
UB Switch
L1-C1-S3
UB Switch
L1-C1-S4
UB Switch
L1-C1-S5
UB Switch
L1-C1-S6
UB Switch
L1-C1-S7
...
Nodes
9-14
omitted
NPU 0
r0
NPU 1
r1
NPU 2
r2
NPU 3
r3
NPU 4
r4
NPU 5
r5
NPU 6
r6
NPU 7
r7
Node 0: K8 FullMesh, 28 direct links
NPU 0
r56
NPU 1
r57
NPU 2
r58
NPU 3
r59
NPU 4
r60
NPU 5
r61
NPU 6
r62
NPU 7
r63
Node 7: K8 FullMesh, 28 direct links
NPU 0
r64
NPU 1
r65
NPU 2
r66
NPU 3
r67
NPU 4
r68
NPU 5
r69
NPU 6
r70
NPU 7
r71
Node 8: K8 FullMesh, 28 direct links
NPU 0
r120
NPU 1
r121
NPU 2
r122
NPU 3
r123
NPU 4
r124
NPU 5
r125
NPU 6
r126
NPU 7
r127
Node 15: K8 FullMesh, 28 direct links
Clos
Clos
Clos
Gray lines: NPU-NPU links. Colored lines: Clos links. All links are bidirectional; crossings are not junctions.

## Slide 2
Node 0: 8 NPUs with a complete 1D FullMesh
Every NPU directly connects to the other 7 NPUs. 8 x 7 / 2 = 28 bidirectional edges.
NPU 0
r0
NPU 1
r1
NPU 2
r2
NPU 3
r3
NPU 4
r4
NPU 5
r5
NPU 6
r6
NPU 7
r7
Each NPU ALSO has 8 separate uplinks to L1-C0-S0 through L1-C0-S7.
Direct FullMesh links and switch uplinks are two separate sets of connections.

## Slide 3
Cabinet 0: each of 64 NPUs connects to all 8 L1 switches
Node 0 and Node 7 are expanded. Nodes 1-6 have identical uplinks and local FullMesh wiring.
UB Switch
L1-C0-S0
UB Switch
L1-C0-S1
UB Switch
L1-C0-S2
UB Switch
L1-C0-S3
UB Switch
L1-C0-S4
UB Switch
L1-C0-S5
UB Switch
L1-C0-S6
UB Switch
L1-C0-S7
NPU 0
r0
NPU 1
r1
NPU 2
r2
NPU 3
r3
NPU 4
r4
NPU 5
r5
NPU 6
r6
NPU 7
r7
Node 0
NPU 0
r56
NPU 1
r57
NPU 2
r58
NPU 3
r59
NPU 4
r60
NPU 5
r61
NPU 6
r62
NPU 7
r63
Node 7
Clos
Per cabinet: 64 x 8 = 512 NPU-L1 links. Each L1 has 64 NPU-facing links and 4 L2-facing links.

## Slide 4
Upper Clos: all 16 L1 switches connect to all 4 L2 switches
Each cabinet has 8 L1 switches. One link per L1-L2 pair gives 16 x 4 = 64 links.
UB Switch
L2-P0-S0
UB Switch
L2-P0-S1
UB Switch
L2-P0-S2
UB Switch
L2-P0-S3
UB Switch
L1-C0-S0
UB Switch
L1-C0-S1
UB Switch
L1-C0-S2
UB Switch
L1-C0-S3
UB Switch
L1-C0-S4
UB Switch
L1-C0-S5
UB Switch
L1-C0-S6
UB Switch
L1-C0-S7
Cabinet 0: 8 L1 switches
UB Switch
L1-C1-S0
UB Switch
L1-C1-S1
UB Switch
L1-C1-S2
UB Switch
L1-C1-S3
UB Switch
L1-C1-S4
UB Switch
L1-C1-S5
UB Switch
L1-C1-S6
UB Switch
L1-C1-S7
Cabinet 1: 8 L1 switches
Clos
No direct L1-L1 or L2-L2 links are defined.
Cross-cabinet path: NPU - local L1 - any L2 - remote L1 - NPU.
Each L2 has 16 populated L1-facing links. Link bandwidths have not been assigned.