## Slide 1
A5 2D-FullMesh + Clos: 128 NPUs / 2 cabinets
8 shared UB switches; each switch connects directly to all 128 NPUs. No additional switch tier.
UB Switch
L1-P0-S0
UB Switch
L1-P0-S1
UB Switch
L1-P0-S2
UB Switch
L1-P0-S3
UB Switch
L1-P0-S4
UB Switch
L1-P0-S5
UB Switch
L1-P0-S6
UB Switch
L1-P0-S7
Clos
Cabinet 0: 8 Nodes x 8 NPUs
X: same Node, all 8 slots (gray)
Y: same slot, all 8 Nodes (green)
...
Nodes
1-6
Cabinet 1: 8 Nodes x 8 NPUs
X: same Node, all 8 slots (gray)
Y: same slot, all 8 Nodes (green)
...
Nodes
9-14
NPU 0
r0
NPU 1
r1
NPU 2
r2
NPU 3
r3
NPU 4
r4
NPU 5
r5
NPU 6
r6
NPU 7
r7
Node 0: all 8 NPUs shown
NPU 0
r56
NPU 1
r57
NPU 2
r58
NPU 3
r59
NPU 4
r60
NPU 5
r61
NPU 6
r62
NPU 7
r63
Node 7: all 8 NPUs shown
NPU 0
r64
NPU 1
r65
NPU 2
r66
NPU 3
r67
NPU 4
r68
NPU 5
r69
NPU 6
r70
NPU 7
r71
Node 8: all 8 NPUs shown
NPU 0
r120
NPU 1
r121
NPU 2
r122
NPU 3
r123
NPU 4
r124
NPU 5
r125
NPU 6
r126
NPU 7
r127
Node 15: all 8 NPUs shown
Direct X/Y links: 40 GB/s. Each NPU-switch uplink: 20 GB/s. All capacities are per direction.

## Slide 2
Cabinet 0: complete 8 x 8 2D-FullMesh wiring
All 64 NPUs and all 448 direct links are shown. Cabinet 1 is identical, with ranks r64-r127.
Node 0
N0 / r0
N1 / r1
N2 / r2
N3 / r3
N4 / r4
N5 / r5
N6 / r6
N7 / r7
Node 1
N0 / r8
N1 / r9
N2 / r10
N3 / r11
N4 / r12
N5 / r13
N6 / r14
N7 / r15
Node 2
N0 / r16
N1 / r17
N2 / r18
N3 / r19
N4 / r20
N5 / r21
N6 / r22
N7 / r23
Node 3
N0 / r24
N1 / r25
N2 / r26
N3 / r27
N4 / r28
N5 / r29
N6 / r30
N7 / r31
Node 4
N0 / r32
N1 / r33
N2 / r34
N3 / r35
N4 / r36
N5 / r37
N6 / r38
N7 / r39
Node 5
N0 / r40
N1 / r41
N2 / r42
N3 / r43
N4 / r44
N5 / r45
N6 / r46
N7 / r47
Node 6
N0 / r48
N1 / r49
N2 / r50
N3 / r51
N4 / r52
N5 / r53
N6 / r54
N7 / r55
Node 7
N0 / r56
N1 / r57
N2 / r58
N3 / r59
N4 / r60
N5 / r61
N6 / r62
N7 / r63
Slot 0
Slot 1
Slot 2
Slot 3
Slot 4
Slot 5
Slot 6
Slot 7
Gray X edges: 8 Nodes x 28 = 224. Green Y edges: 8 slots x 28 = 224.
14 direct neighbors per NPU; 40 GB/s per direct link. Crossings are not junctions.

## Slide 3
Two independent mesh dimensions: each NPU has 7 + 7 direct neighbors
X = same Node / different slot. Y = same cabinet / same slot / different Node.
Node 0
NPU 0 / r0
Node 0
NPU 1 / r1
Node 0
NPU 2 / r2
Node 0
NPU 3 / r3
Node 0
NPU 4 / r4
Node 0
NPU 5 / r5
Node 0
NPU 6 / r6
Node 0
NPU 7 / r7
X: Node 0 complete mesh
8 NPUs / 28 direct links / 40 GB/s per link
Node 0
NPU 0 / r0
Node 1
NPU 0 / r8
Node 2
NPU 0 / r16
Node 3
NPU 0 / r24
Node 4
NPU 0 / r32
Node 5
NPU 0 / r40
Node 6
NPU 0 / r48
Node 7
NPU 0 / r56
Y: slot 0 across Nodes 0-7
8 NPUs / 28 direct links / 40 GB/s per link
Example r0: X neighbors r1-r7; Y neighbors r8, r16, r24, r32, r40, r48, r56.

## Slide 4
Global Clos: 8 shared switches, 8 separate uplinks per NPU
Node 0 and Node 8 are expanded. All other Nodes have exactly the same switch uplinks.
UB Switch
L1-P0-S0
UB Switch
L1-P0-S1
UB Switch
L1-P0-S2
UB Switch
L1-P0-S3
UB Switch
L1-P0-S4
UB Switch
L1-P0-S5
UB Switch
L1-P0-S6
UB Switch
L1-P0-S7
Clos
NPU 0
r0
NPU 1
r1
NPU 2
r2
NPU 3
r3
NPU 4
r4
NPU 5
r5
NPU 6
r6
NPU 7
r7
Cabinet 0 / Node 0
NPU 0
r64
NPU 1
r65
NPU 2
r66
NPU 3
r67
NPU 4
r68
NPU 5
r69
NPU 6
r70
NPU 7
r71
Cabinet 1 / Node 8
128 x 8 = 1024 bidirectional NPU-switch links. No switch-switch links.
Each link = 20 GB/s per direction. Each NPU has 8 x 20 = 160 GB/s switch-facing capacity.
Each switch has 128 populated downlinks; nominal aggregate ingress capacity = 2560 GB/s.

## Slide 5
Topology 3: ranks, switches and link definitions
Contest topology based on the UB-Mesh 2D-FullMesh design; user-specified 8-switch fabric.
Rank mapping
r = 64 x cabinet + 8 x local Node + slot; global Node = 8 x cabinet + local Node.
X dimension
Within each Node: every pair of its 8 NPUs connects directly; 16 x 28 = 448 links.
Y dimension
Within each cabinet and slot: every pair of 8 Nodes connects directly; 2 x 8 x 28 = 448 links.
Switch fabric
Each rank r0-r127 connects to each UB Switch L1-P0-S0 through L1-P0-S7; 1024 links.
Bandwidth
X/Y: UB x4 -> 40 GB/s. Each switch uplink: UB x2 -> 20 GB/s; 8 ports total UB x16.
Conversion assumption
UB lane = 10 GB/s per direction, carried over from Topology 2; not a quoted device specification.
Timing / data
Startup = 1 us; switch processing = 0.3 us per traversed switch; 1 MB/rank; splits [1,2,4].
Source
UB-Mesh, arXiv:2503.20377: Figure 7 / Section 3.3.1 (UB x56); Section 6.3 (default UB x16).