## Slide 1
GB200 NVL72: 144 GPUs / 2 racks / 4 compute rails
Rack-local NVLink domains and inter-rack NDR400 compute fabric are separate networks.
IB Spine
L2-P0-S0
IB Spine
L2-P0-S1
IB Spine
L2-P0-S2
IB Spine
L2-P0-S3
IB Spine
L2-P0-S4
IB Spine
L2-P0-S5
IB Spine
L2-P0-S6
IB Spine
L2-P0-S7
IB Spine
L2-P0-S8
Rail 0: slot 0 on every compute tray
IB Leaf
Leaf-C0-R0
IB Leaf
Leaf-C1-R0
18 GPUs per Leaf; 1 x 400 Gb/s per GPU
Rail 1: slot 1 on every compute tray
IB Leaf
Leaf-C0-R1
IB Leaf
Leaf-C1-R1
18 GPUs per Leaf; 1 x 400 Gb/s per GPU
Rail 2: slot 2 on every compute tray
IB Leaf
Leaf-C0-R2
IB Leaf
Leaf-C1-R2
18 GPUs per Leaf; 1 x 400 Gb/s per GPU
Rail 3: slot 3 on every compute tray
IB Leaf
Leaf-C0-R3
IB Leaf
Leaf-C1-R3
18 GPUs per Leaf; 1 x 400 Gb/s per GPU
Rack 0: 72 GPUs / 18 compute trays
9 switch trays = 18 NVSwitch ASICs
Each GPU has 18 NVLinks + one 400 Gb/s NIC
Trays 0, 1, 17 expanded below. Trays 2-16 omitted.
NVSwitch
NV-C0-S0
NVSwitch
NV-C0-S1
NVSwitch
NV-C0-S2
NVSwitch
NV-C0-S3
NVSwitch
NV-C0-S4
NVSwitch
NV-C0-S5
NVSwitch
NV-C0-S6
NVSwitch
NV-C0-S7
NVSwitch
NV-C0-S8
NVSwitch
NV-C0-S9
NVSwitch
NV-C0-S10
NVSwitch
NV-C0-S11
NVSwitch
NV-C0-S12
NVSwitch
NV-C0-S13
NVSwitch
NV-C0-S14
NVSwitch
NV-C0-S15
NVSwitch
NV-C0-S16
NVSwitch
NV-C0-S17
Compute Tray 0
GPU
r0
GPU
r1
GPU
r2
GPU
r3
Compute Tray 1
GPU
r4
GPU
r5
GPU
r6
GPU
r7
Compute Tray 17
GPU
r68
GPU
r69
GPU
r70
GPU
r71
Rack 1: 72 GPUs / 18 compute trays
9 switch trays = 18 NVSwitch ASICs
Each GPU has 18 NVLinks + one 400 Gb/s NIC
Trays 0, 1, 17 expanded below. Trays 2-16 omitted.
NVSwitch
NV-C1-S0
NVSwitch
NV-C1-S1
NVSwitch
NV-C1-S2
NVSwitch
NV-C1-S3
NVSwitch
NV-C1-S4
NVSwitch
NV-C1-S5
NVSwitch
NV-C1-S6
NVSwitch
NV-C1-S7
NVSwitch
NV-C1-S8
NVSwitch
NV-C1-S9
NVSwitch
NV-C1-S10
NVSwitch
NV-C1-S11
NVSwitch
NV-C1-S12
NVSwitch
NV-C1-S13
NVSwitch
NV-C1-S14
NVSwitch
NV-C1-S15
NVSwitch
NV-C1-S16
NVSwitch
NV-C1-S17
Compute Tray 0
GPU
r72
GPU
r73
GPU
r74
GPU
r75
Compute Tray 1
GPU
r76
GPU
r77
GPU
r78
GPU
r79
Compute Tray 17
GPU
r140
GPU
r141
GPU
r142
GPU
r143
CX-7
400G
GPU
r0
r0: 18 NVLink connections, each 50 GB/s
All other GPUs have the same connection pattern
All Leaves connect to all 9 shared Spines. Each Leaf-Spine pair: 2 x 400 Gb/s = 100 GB/s per direction.
Highlighted r0: orange = 18 NVLinks; blue = 1 NIC/Leaf uplink. Other GPU connections omitted on this overview.

## Slide 2
Inside Rack 0: all 72 GPUs connect to all 18 NVSwitch ASICs
18 compute trays x 4 GPUs. 9 NVLink switch trays x 2 ASICs. Every GPU-ASIC link is drawn.
NVSwitch
NV-C0-S0
NVSwitch
NV-C0-S1
NVSwitch
NV-C0-S2
NVSwitch
NV-C0-S3
NVSwitch
NV-C0-S4
NVSwitch
NV-C0-S5
NVSwitch
NV-C0-S6
NVSwitch
NV-C0-S7
NVSwitch
NV-C0-S8
NVSwitch
NV-C0-S9
NVSwitch
NV-C0-S10
NVSwitch
NV-C0-S11
NVSwitch
NV-C0-S12
NVSwitch
NV-C0-S13
NVSwitch
NV-C0-S14
NVSwitch
NV-C0-S15
NVSwitch
NV-C0-S16
NVSwitch
NV-C0-S17
Complete bipartite connection: 72 GPUs x 18 NVSwitch ASICs = 1296 links
Each link: 50 GB/s per direction. Rack 1 has the same connections for ranks r72-r143.
Compute Tray 0
GPU
r0
GPU
r1
GPU
r2
GPU
r3
Compute Tray 1
GPU
r4
GPU
r5
GPU
r6
GPU
r7
Compute Tray 2
GPU
r8
GPU
r9
GPU
r10
GPU
r11
Compute Tray 3
GPU
r12
GPU
r13
GPU
r14
GPU
r15
Compute Tray 4
GPU
r16
GPU
r17
GPU
r18
GPU
r19
Compute Tray 5
GPU
r20
GPU
r21
GPU
r22
GPU
r23
Compute Tray 6
GPU
r24
GPU
r25
GPU
r26
GPU
r27
Compute Tray 7
GPU
r28
GPU
r29
GPU
r30
GPU
r31
Compute Tray 8
GPU
r32
GPU
r33
GPU
r34
GPU
r35
Compute Tray 9
GPU
r36
GPU
r37
GPU
r38
GPU
r39
Compute Tray 10
GPU
r40
GPU
r41
GPU
r42
GPU
r43
Compute Tray 11
GPU
r44
GPU
r45
GPU
r46
GPU
r47
Compute Tray 12
GPU
r48
GPU
r49
GPU
r50
GPU
r51
Compute Tray 13
GPU
r52
GPU
r53
GPU
r54
GPU
r55
Compute Tray 14
GPU
r56
GPU
r57
GPU
r58
GPU
r59
Compute Tray 15
GPU
r60
GPU
r61
GPU
r62
GPU
r63
Compute Tray 16
GPU
r64
GPU
r65
GPU
r66
GPU
r67
Compute Tray 17
GPU
r68
GPU
r69
GPU
r70
GPU
r71
No direct GPU-GPU mesh edges, no NVSwitch-NVSwitch links, and no NVLink links between the two racks.

## Slide 3
Compute Tray 0: 4 GPUs, 4 NICs, 4 separate rails
GPU slot j uses rail j. The GPU-NIC-Leaf path is one logical edge in the input, with 400 Gb/s capacity.
IB Leaf
Leaf-C0-R0
ConnectX-7
400 Gb/s
GPU
r0
GPU
r0
50 GB/s per direction
IB Leaf
Leaf-C0-R1
ConnectX-7
400 Gb/s
GPU
r1
50 GB/s per direction
IB Leaf
Leaf-C0-R2
ConnectX-7
400 Gb/s
GPU
r2
50 GB/s per direction
IB Leaf
Leaf-C0-R3
ConnectX-7
400 Gb/s
GPU
r3
50 GB/s per direction
NVSwitch
NV-C0-S0
NVSwitch
NV-C0-S1
NVSwitch
NV-C0-S2
NVSwitch
NV-C0-S3
NVSwitch
NV-C0-S4
NVSwitch
NV-C0-S5
NVSwitch
NV-C0-S6
NVSwitch
NV-C0-S7
NVSwitch
NV-C0-S8
NVSwitch
NV-C0-S9
NVSwitch
NV-C0-S10
NVSwitch
NV-C0-S11
NVSwitch
NV-C0-S12
NVSwitch
NV-C0-S13
NVSwitch
NV-C0-S14
NVSwitch
NV-C0-S15
NVSwitch
NV-C0-S16
NVSwitch
NV-C0-S17
Each GPU has one NVLink to EACH of the 18 NVSwitch ASICs below
18 x 50 = 900 GB/s NVLink per direction per GPU. Compute NIC: 1 x 50 GB/s per direction per GPU.

## Slide 4
Inter-rack Clos: all 4 rails, all 8 Leaves, all 9 shared Spines
This 144-GPU contest instance populates 2 racks of the reference multi-rail topology.
IB Spine
L2-P0-S0
IB Spine
L2-P0-S1
IB Spine
L2-P0-S2
IB Spine
L2-P0-S3
IB Spine
L2-P0-S4
IB Spine
L2-P0-S5
IB Spine
L2-P0-S6
IB Spine
L2-P0-S7
IB Spine
L2-P0-S8
IB Leaf
Leaf-C0-R0
IB Leaf
Leaf-C1-R0
Rail 0
IB Leaf
Leaf-C0-R1
IB Leaf
Leaf-C1-R1
Rail 1
IB Leaf
Leaf-C0-R2
IB Leaf
Leaf-C1-R2
Rail 2
IB Leaf
Leaf-C0-R3
IB Leaf
Leaf-C1-R3
Rail 3
Clos
Each Leaf-Spine edge aggregates 2 x 400 Gb/s links: 100 GB/s per direction.
Per Leaf: 18 GPU-facing ports x 50 = 900 GB/s; 9 Spine bundles x 100 = 900 GB/s.
Spines are shared across rails. Cross-rail paths traverse a Spine. No Leaf-Leaf or Spine-Spine edges.

## Slide 5
Every GPU NIC connects to exactly one rail Leaf
Rank mapping: r = 72 x rack + 4 x tray + slot. Rail = slot = rank modulo 4.
IB Leaf
Leaf-C0-R0
GPU
r0
GPU
r4
GPU
r8
GPU
r12
GPU
r16
GPU
r20
GPU
r24
GPU
r28
GPU
r32
GPU
r36
GPU
r40
GPU
r44
GPU
r48
GPU
r52
GPU
r56
GPU
r60
GPU
r64
GPU
r68
IB Leaf
Leaf-C1-R0
GPU
r72
GPU
r76
GPU
r80
GPU
r84
GPU
r88
GPU
r92
GPU
r96
GPU
r100
GPU
r104
GPU
r108
GPU
r112
GPU
r116
GPU
r120
GPU
r124
GPU
r128
GPU
r132
GPU
r136
GPU
r140
Rail 0: 18 GPUs/rack, 36 GPUs total; each GPU uplink = 400 Gb/s = 50 GB/s
IB Leaf
Leaf-C0-R1
GPU
r1
GPU
r5
GPU
r9
GPU
r13
GPU
r17
GPU
r21
GPU
r25
GPU
r29
GPU
r33
GPU
r37
GPU
r41
GPU
r45
GPU
r49
GPU
r53
GPU
r57
GPU
r61
GPU
r65
GPU
r69
IB Leaf
Leaf-C1-R1
GPU
r73
GPU
r77
GPU
r81
GPU
r85
GPU
r89
GPU
r93
GPU
r97
GPU
r101
GPU
r105
GPU
r109
GPU
r113
GPU
r117
GPU
r121
GPU
r125
GPU
r129
GPU
r133
GPU
r137
GPU
r141
Rail 1: 18 GPUs/rack, 36 GPUs total; each GPU uplink = 400 Gb/s = 50 GB/s
IB Leaf
Leaf-C0-R2
GPU
r2
GPU
r6
GPU
r10
GPU
r14
GPU
r18
GPU
r22
GPU
r26
GPU
r30
GPU
r34
GPU
r38
GPU
r42
GPU
r46
GPU
r50
GPU
r54
GPU
r58
GPU
r62
GPU
r66
GPU
r70
IB Leaf
Leaf-C1-R2
GPU
r74
GPU
r78
GPU
r82
GPU
r86
GPU
r90
GPU
r94
GPU
r98
GPU
r102
GPU
r106
GPU
r110
GPU
r114
GPU
r118
GPU
r122
GPU
r126
GPU
r130
GPU
r134
GPU
r138
GPU
r142
Rail 2: 18 GPUs/rack, 36 GPUs total; each GPU uplink = 400 Gb/s = 50 GB/s
IB Leaf
Leaf-C0-R3
GPU
r3
GPU
r7
GPU
r11
GPU
r15
GPU
r19
GPU
r23
GPU
r27
GPU
r31
GPU
r35
GPU
r39
GPU
r43
GPU
r47
GPU
r51
GPU
r55
GPU
r59
GPU
r63
GPU
r67
GPU
r71
IB Leaf
Leaf-C1-R3
GPU
r75
GPU
r79
GPU
r83
GPU
r87
GPU
r91
GPU
r95
GPU
r99
GPU
r103
GPU
r107
GPU
r111
GPU
r115
GPU
r119
GPU
r123
GPU
r127
GPU
r131
GPU
r135
GPU
r139
GPU
r143
Rail 3: 18 GPUs/rack, 36 GPUs total; each GPU uplink = 400 Gb/s = 50 GB/s
All 144 GPU-to-Leaf edges are drawn. NICs are collapsed into these logical links in TXT/JSON.

## Slide 6
Topology 4: exact link model and bandwidth units
GB200 NVL72 + ConnectX-7 / Quantum NDR400. All edge capacities are unidirectional.
Inventory
144 GPUs, 36 NVSwitch ASICs, 8 IB Leaves, 9 shared IB Spines. 2808 bidirectional logical edges.
GPU to NVSwitch
Every GPU connects to all 18 ASICs in its rack: 18 x 50 = 900 GB/s per direction.
GPU to IB Leaf
One 400 Gb/s NIC per GPU, rail = slot. Each Leaf has 18 GPU-facing links: 18 x 50 = 900 GB/s.
Leaf to Spine
Every Leaf connects to every Spine via 2 x 400 Gb/s: 100 GB/s aggregate per direction per pair.
Packet / chunk model
Leaf-Spine bundles can stripe packets over both ports. Semantic chunks may be split into [1,2,4] parts.
Scope
The 2-rack population and retained 9 shared Spines are a contest adaptation of the supplied 8-rack diagram.
Timing
1 us per logical send startup, 0.3 us per traversed switch. Contest parameters, not vendor measured latency.
Sources
NVIDIA DGX GB200 SuperPOD Reference Architecture, Network Fabrics / Key Components; DGX GB hardware guide.